## Slide 1
CAT XE wheel loaders
CAT 966 XE_972 XE

## Slide 2
Main component of XE wheel loaders is Cat designed and built CVT transmission which combines the efficiency of a mechanical transmission, with the reactivity of a small hydraulic variator
Benefits of XE transmission:
Best in class fuel efficiency, up to 25% savings
Eliminates torque converter loss thanks to power-split transmission
Controls machine driving speed and desired rimpull independently from engine RPM - machine automatically adjusts RPM depending on task at hand (allows advanced rimpull control)
Lower engine speed gives lower fuel burn, less noise and longer life of engine components
Smart Deceleration / Retarding - transfers engine braking power to the hydraulic system contributing to lower fuel consumption and less brake wear
Hill hold - no need to press brake pedal to stay in the same position on the grade
Engine
Mechanical Path
Variator
Planetary
Gear Sets
Drive Shaft
Power Split
XE – Optimizes power flow through the transmission providing best in class fuel efficiency

## Slide 3: Assist functions
NextGen wheel loaders come with a range of proven and new ASSIST functions. This helps the operator in his daily work and enables inexperienced machinists to work efficiently Saving kickout points (automatic blade return to chosen location)
Auto-Set-Tires (automatic traction control) providing less tire wear, reduced fuel burn, lower dig time, bigger payload. AutoDig (automatic bucket filling)
JOB Aids – Dig cycle counter; wheel revolution counter, etc. Adjustable machine speed limit

## Slide 4
Efficient thanks to the integrated weighing system
No risk of the truck being overloaded
Easy operation via Touch Screen
  Cat Payload – integrated scale weighing system
  Very accurate weighing of the load quantity, never overloaded truck
  Evaluation of the loaded tons/liters of diesel. Data available via Vision link
  “on-the-go” weighing system
5.8
12.4

## Slide 5
  List Management - Materials and trucks can be saved
  Tip Off Assist - automatic reweighing
  Multitask mode
  Manual add mode
CAT Advanced Payload (optional)

## Slide 6
Unique ease of use joystick steering
Unique joystick steering without a steering wheel for the best visibility
The only system on the market with road approval up to 40km/h – so good and reliable (950-966)
Load-sensing and position-sensitive (joystick position equals steering angle). This means that no counter-steering is necessary

## Slide 7: Next Gen Seat – increased Comfort
  Standard: Deluxe - heated
  - mechanical lumbar support
  Optional: Premium
  - Heated and cooled
  - pneumatic lumbar support
  Suspension innovation (standard in joystick steering):
  - increases damping at the top and bottom of the suspension travel to avoid hard stops
Up to 30% reduced vibrations

## Slide 8
Safety thanks to good accessibility
Problem-free driver changes through simplicity
Platform for window cleaning
Handrail around cabin for maximum safety
Color monitor for rear view camera, optional 360º camera
Quiet cabin at 68 dBA

## Slide 9
Comfort and safety
  Very finely controllable, electro-hydraulic seat mounted implement controls
  Clearly designed dashboard and best arrangement of the controls
  Remote door opening activation from the floor
  Inclined ladder for comfortable ascent and descent
  5 cm increased legroom compared to previous gen loaders

## Slide 10
Cost-saving through easy maintenance
All important service points are easily and safely accessible from the ground which means minimized chance of accidents
Few service points simplify maintenance
Maintenance center with all filters and measuring points for quick service and diagnosis

## Slide 11
Short downtimes because it requires very little maintenance
Low consumption thanks to the latest CAT engine technology
Low fuel costs due to low engine speed
Low consumption, reliable CAT 6 cylinder diesel engine C9.3B
Latest engine technology meets Stage V
Programmable idle/automatic shutdown reduces idle time and ensures cooling of turbo and other engine parts
ECO mode for maximum performance at low speeds
Passive regeneration – simple, reliable and service free solution invisible to the operator
Non-EGR air system for improved reliability

## Slide 12
Maximum productivity through optimized tools
  Cat Performance series buckets
  Long floor, wide opening allows material to be loaded faster
  Rounded side walls, raised rear wall with integrated spill guard
  Better material retention therefore higher fill factor
  Fast penetration resulting in shorter cycle times

## Slide 13
Visionlink – complete visibility for entire fleet
Maximize uptime
Monitor equipment health, fault codes, fluid analysis, and inspection due dates
Reduce unplanned downtime with critical alerts
Order parts and schedule service within the platform.
Optimize utilization
Manage according to projects, groups, or geofences
Set utilization targets and monitor performance
Make informed, data-based decisions to reduce operating costs.

## Slide 14
CAT Financial financing solutions for best liquidity
Fixed service costs create clear conditions
Financial leasing:
Period from 12 to 60 months
Down payment: from 10%
Fixed interest rate
Payment schedule tailored to your needs and business specifics
Long-term rental:
Period from 12 to 60 months
Down payment: from 0%
Maintenance costs included in the fixed monthly payment
Option to buy back the equipment at the end of the rental contract
Financing of service products:
Allows you to purchase repairs, certified rebuild services or work tools on hire purchase
Term from 6 to 60 months
Down payment: from 0%
Fixed interest rate

## Slide 15
For more information please contact your local Avesco dealer